## Slide 1
Vinyl Machine

## Slide 2
Table of Content:
Introduction and models
Why we need this machine/ Use-fullness
Vinyl machine types
Vinyl machine specification
Machine installation
Software requirement
Vinyl Machine working steps
Material , Speed, Power requirement
Safety precautions
Machine Maintenance
Training and promotion
Machine selection/ comparison

## Slide 3
We Can Do Following things with Vinyl cutting Machine
Projects

## Slide 4
Introduction:
X-Y Plotting machine which can cut name on radium paper also we can print
Circuit on copper adhesive paper.
Vinyl cutter Camm1 CX24:
Engraving tool holder
Blade assembly

## Slide 5
Need of Machine / Use-fullness :
Converts prototype into products
Training and business
Makes ideas into reality
Machine makes machine
Resolution, Accuracy differs it from Handmade .

## Slide 6
Roland DGA corporation:
Driving method- Digital control servo motor:
Cutting method-Media-moving method;
Media width - 2” to 27.5”(50 to 700mm)
Cutting speed - -4 to 20ips (10 to500mm/sec)
Blade force - 30 to 250gf; Mechanical
resolution - 0.000984” (0.025mm)
Printing and cutting when loading printed material –
(1) (3) (+/- 1mm)
Machine specification

## Slide 7
Design software
FAB Modules
Machine software
AutoCAD
any 2D design software
Inkscape
SOFTWARE
File formats: .png
Dr.sticka plus
Dr.sticka plus
Cutstudio
Illustrator
Roland Driver

## Slide 8
Working steps
Make design file ready
Import design file inside
Machine software-upload
Start printing & after printing remove material
Adjust X-Y axis plane on machine
Start machine and
check alignment of bed
Fixed cu or radium paper inside

## Slide 9
Material can be printed:
Copper adhesive paper
Vinyl paper, radium paper
Applications:
Making flexible PCB
Invitation card, Office card
T shirt printing
Screen printing
Number plate, decoration things

## Slide 10
Use brush or vacuum cleaner after you finished
Clean rods with rust cleaner in every day, use specified drill bits
Use of align key must
Check all connection wiring every week
Maintenance
Maintain maintenance
box
Clean machine after every use
Sensor should be clean
Remove unwanted material from blade after use